## Slide 1
3D Anatomy Segmentation using
Perceptual Computing
Shlomo Shenzis1, Moshe Samson1, Refael Vivanti1
The Rachel and Selim Benin School of Computer Science and Engineering The Hebrew University of Jerusalem
Email: shlomo.shenzis@mail.huji.ac.il moshe.samson@mail.huji.ac.il
refael.vivanti@mail.huji.ac.il
Input:
CT slices IMAGES?
Hand motion and gestures acquired by the Leap Motion
  A 3D approximate scribble across several slices of the CT scan
  A 3D correction scribble of the segmentation leaks over the output mesh
Output:
2D – Correct segmentation of the anatomy.
3D – Mesh of the corrected anatomy.
Motivation
    The delineation and segmentation of anatomical structures and pathologies in volumetric scans is a challenging and time-consuming task that significantly hampers the use of 3D models in the clinic.
    Today, radiologists estimates the tumor size using linear measurements on individual 2D CT scan slices.
    The problems: not accurate, time-consuming and tedious.
    Our solution: a semi-automatic tool for 3D segmentation in volumetric medical scans using natural input from the user.
    Stage 2: Segmentation
    Online segmentation of the structure of interest with the Grow-Cut segmentation algorithm over the given initial scribble and real-time 2D corrections.
    When repeating this stage, additional scribbles can be added at any time.
    Output may be leaky, and inaccurate.
    Leaks are in 3D, not in 2D, therefore requiring 3D correction method.
    IMAGES
Stage 3: Correction Scribble on 3D mesh
Annotate leaks versus correct regions on the 3D anatomy mesh using two-point defined, shortest geodesic path scribbles.
IMAGES
Validation:
  10 cases from 10 different patients
    resolution range is: ???
  Ground truth – Radiologists approved segmentation on CT.
  Comparison metrics:
    DICE volumetric overlap error (VOE)
    Volumetric Similarity (VS)
    Average Hausdorff Distance (AHD)
Summary:
Semi-automatic 3D anatomy segmentation method using Natural Input.
Grow-Cut algorithm for 2D segmentation.
Graph based lesion removal algorithm using contour smoothness.
???% Volume Overlap Error
Segmentation challenges
Soft-tissues segmentation values are usually very similar to each other.
      Kidney – 30 HU
      Liver – 40-60 HU
  Tumor-to-liver contrast: ~30 HU
Quality and Resolution – very often, the CT is in medium to poor resolution, which causes artifacts in the results.
Stage 1: Initial Scribble on 2D Slices
    Acquire initial, approximate 2D scribbles on the anatomy for the foreground and background.
    Natural Input – input acquired by natural interaction with the user:
      Hand gestures
      Finger tracking
    IMAGEs
Repetition: Repeating Stage 1-2, 3-4
Iteratively repeat stages 1-2,2-4 until a satisfying result is obtained.
Corrections can be done at any stage, in both 2D and 3D views.
Method stages:
Initial Scribble on 2D slices
Segmentation [Optional repeat of stages 1-2]
Corrections scribble on 3D mesh
Segmentation lesions removal [Optional repeat of stages 3-4]
Results
 | VOE[%] | VS[%] | AHD[mm]
Mean |  |  | 
Std |  |  | 
Min |  |  | 
Max |  |  | 
Stage 4: Leaks Removal
3D correction of the segmentation lesions using a graph based segmentation algorithm.
Lesions removal algorithm – contour smoothness value used in order to ‘shrink’ leaks and ‘fill’ holes.